## Slide 1
Hello everyone, my name is Raymond and my project is “real-time diagnostic tools for the scanning electron microscope”. I am supervised by Dr David Holburn.

## Slide 2
The scanning electron microscope is a type of microscope that uses electrons as a probe, and this slide shows its basic construction. Because of the shorter wavelength of electrons, they can have much higher resolution than traditional optical microscopes. This is beneficial for many fields because it allows scientists to observe very small details that were previously impossible to see.
It is a complex instrument to use, and operators often need intensive training and practical experience to be able to capture images of good quality. So, the aim of the project is to develop a diagnostic tool that aids them.

## Slide 3
The tool I developed has two main features---it calculates the histogram and FFT of the image and displays the results in real-time.
The histogram and FFT provide operators a more straightforward way for studying structures of the specimen.
The importance of being real-time is that it allows operators to see the information while constantly changing settings of the SEM, and thus improves their productivity.
The algorithms are actually widely used in the field, but in the past, they were mostly only possible offline. In 1998, to calculate the FFT of a 1000 by 1000 image, people could only get 0.6 frames per second using the most advanced CPU at the time.

## Slide 4
Achieving real-time calculation was the most important focus of the project, and it was made possible by the use of GPUs.
The architecture of the GPU emphasises on parallelism. This comes from the requirements in rendering images on a display. To render an image, the GPU divides it into fragments---as you can see on the screen- and uses a large matrix of parallel processing cores to do the calculation for each fragment independently.
This makes them much faster than CPUs at many general-purpose computing tasks. For example, at vector additions. A thread may be executed 10 times faster on a CPU, but there might be 1000 times more threads running on a GPU, which makes the GPU 100 times faster overall.

## Slide 5
I did a test on vector addition to compare the performance of the GPU and CPU on my own laptop. I would say it’s a middle-range laptop, so I'm not using crazily fast special GPUs. I used NVIDIA’s CUDA toolkit to program the GPU. As you can see, the GPU is more than 1000 times faster than the CPU. The blue line does have a gradient, but the numbers are in the order of nanosecond so you can’t see it.
This gain in performance allowed my tool to do real-time calculations.
An especially important application of FFT is to use it for evaluating the astigmatism of SEM images.

## Slide 6
Astigmatism describes the phenomenon that the image appears stretched due to imperfections in the lens system. An important property of it is that the direction of stretching rotates as the image goes from being under-focused to over-focused, as shown on the screen. As a result, the FFT of the image also rotates.
So, we can use the FFT to evaluate astigmatism. This is very helpful because it eliminates the subjectivity in using the original image.
To use the FFT for this purpose, the calculation has to be real-time since operators need to see the result immediately as they change the focusing of the SEM.

## Slide 7
Here are some screenshots of the software. The operator can use these buttons to open and close windows for different plots, and to apply a Hanning window or histogram equalisation.
This is a sample SEM image, and these are its FFT and histogram. The software is written in Python and I am currently getting about 10 frames per second. If better performance is needed, it is very easy to translate it into C++.
I also used the tool to implement an automatic focusing and astigmatism correction algorithm, but because of the Covid-19, I haven’t been able to comprehensively test its performance.

## Slide 8
This slide shows the result of focusing correction done by the algorithm. It was able to find the same best focus setting as determined by an operator. More tests need to be done to see how good it is at correcting astigmatism.